## Slide 1
MARVELL
CXL Memory for LLM Inference Staging
via an On-Device DMA Controller
Veerasenareddy Burru · Pradeep Kumar Nalla · Alok Prasad · Satananda Burla
Marvell Technology · 18th ACM Workshop on Hot Topics in Storage & File Systems (HotStorage '26) · Prague · Sep 28–29, 2026
1 The Problem
2 Our Approach & Method
How an LLM serves a request
Prompt
user input
Generate token
one model step
Append K,V
store in KV cache
repeat every token
Each token reuses the cached keys & values of all earlier tokens — the KV cache.
The KV cache grows with output length and number of concurrent users.
The KV cache fills GPU memory
HBM capacity
Model
weights
KV cache
Light load
Model
weights
KV cache
Heavy load
HBM holds fixed weights plus the growing KV cache.
Capacity — not compute — often caps how many requests you can serve.
When HBM fills, inference must shrink work, recompute, or spill off-GPU.
Shrink
cap batch / context
Recompute
waste GPU cycles
Spill off-GPU
if a tier is fast enough
Why today's spill options fall short
Host DRAM
CPU + IOMMU overhead; a host-DRAM bounce; shares the bus with other traffic.
NVMe via GDS
Built for bulk block I/O — slow & high-latency on small, frequent transfers.
RDMA
Network-oriented and coarse-grained; throughput gated by network latency.
What KV-cache staging needs
Near-link bandwidth · low latency · host-bypass
Fine-grained 4 KB–128 KB access on a dedicated path
Direct GPU access to CXL memory
1
P2P DMA
The expander's DMA controller drives every transfer against GPU HBM; the GPU is passive.
2
Full host bypass
No host DRAM, CPU, or IOMMU on the data path — a pure PCIe switch-domain transfer.
3
Framework-compatible
Appears as a GDS-style tier: no changes to vLLM, FlexGen, or NIXL.
How it works: full host bypass
GPU HBM
Shared PCIe switch
CXL expander (DMA)
The expander's DMA controller is the active party in every transfer.
GPU-facing traffic is plain PCIe P2P — CXL is used only host-side for capacity & management.
Data Path
Experimental setup
GPU
NVIDIA H200 NVL
CXL expander
Marvell Structera A — on-device DMA controller
Expander memory
128 GB DDR5, 8 channels
Interconnect
PCIe Gen5 ×16 · shared PCIe switch
NVMe baseline
4× PCIe Gen5 ×4 SSDs (aggregate)
Host
AMD EPYC 9555 · 768 GB · Ubuntu 24.04 · CUDA 13.1
3 Results · CXL.DMA-P2P vs. NVMe-backed GDS
51 GB/s
Peak read bandwidth
29.7 GB/s
Peak write bandwidth
3–4 µs
Read/write latency in KV range
> 10×
Lower latency than NVMe/GDS
Chart: Block size
| 4KB | 8KB | 16KB | 32KB | 64KB | 128KB | 256KB | 512KB | 1MB | 2MB | 4MB | 8MB
CXL.DMA-P2P | 1.4 | 2.6 | 4.6 | 10 | 19 | 35.9 | 48 | 50 | 50.6 | 51 | 51 | 50.6
CXL.DAX | 0.7 | 1.3 | 4.5 | 10 | 14 | 28 | 42 | 47 | 49 | 50 | 50 | 50
GDS / NVMe (×4) | 0.2 | 0.4 | 0.85 | 1.8 | 3.2 | 5.1 | 9 | 15 | 20.5 | 26 | 30 | 31.6
Host DRAM | 2.1 | 5 | 10 | 14 | 14.5 | 14.5 | 14.5 | 14.5 | 14.5 | 14.5 | 14.5 | 14.5
KV cache range
PCIe Gen5 ×16 ≈ 64 GB/s
Read bandwidth vs. block size
Chart: Block size
| 4KB | 8KB | 16KB | 32KB | 64KB | 128KB | 256KB | 512KB | 1MB | 2MB | 4MB | 8MB
CXL.DMA-P2P | 1.3 | 2.5 | 3.7 | 9 | 17 | 29.7 | 29.5 | 29 | 28.4 | 29.7 | 29 | 28.3
CXL.DAX | 0.7 | 0.9 | 1.6 | 3.7 | 7.5 | 20.7 | 29 | 37 | 42 | 46 | 48 | 50
GDS / NVMe (×4) | 0.25 | 0.5 | 1 | 1.8 | 3.2 | 5.8 | 10 | 15.5 | 21.6 | 27.5 | 30 | 31.1
Host DRAM | 2 | 4.5 | 9 | 18 | 24 | 26 | 26 | 26 | 26 | 26 | 26 | 26
KV cache range
PCIe Gen5 ×16 ≈ 64 GB/s
Write bandwidth vs. block size
Chart: Block size
| 4KB | 8KB | 16KB | 32KB | 64KB | 128KB | 256KB | 512KB | 1MB | 2MB | 4MB | 8MB
CXL.DMA-P2P (read) | 2.9 | 3 | 3.1 | 3.3 | 3.5 | 3.7 | 7.9 | 13.1 | 23.4 | 44.3 | 85.4 | 167.9
CXL.DMA-P2P (write) | 3.1 | 3.3 | 3.5 | 3.8 | 4.1 | 4.4 | 9.8 | 16.8 | 31 | 61.2 | 135.6 | 287.3
GDS / NVMe (read) | 52.3 | 54 | 56 | 60 | 66 | 72.5 | 95 | 130 | 175 | 230 | 280 | 311
KV cache range
End-to-end latency vs. block size
NVMe baseline: 4× PCIe Gen5 ×4 SSDs (aggregate). Host DRAM measured on a shared PCIe bus with concurrent traffic. Dashed line = Gen5 ×16 link ceiling.
Key takeaways
Reaches CXL memory over PCIe P2P DMA — no GPU changes.
High bandwidth, close to the Gen5 link on reads.
Order-of-magnitude lower latency than NVMe/GDS.
Biggest wins at KV-cache block sizes (4 KB–128 KB).
Future work
Write-path optimization: pipelining & write-combining.
Share one expander across GPUs / tenants.
On-expander KV compression; end-to-end in vLLM / TensorRT-LLM.
Related work — where we fit
LLM memory mgmt (vLLM, FlexGen, Mooncake): we add a faster spill tier.
GPU storage offload (GDS, InstInfer): same host-bypass, faster medium.
CXL + GPU (Pond, CXL-GPU, LMB): no GPU changes — pure PCIe P2P.
Paper: https://doi.org/10.1145/3837053.3837356
{vburru, pnalla, palok, sburla}@marvell.com
Essential technology, done right™
NIXL ODM
plugin
user space
Marvell
kernel module
kernel space
Structera A · Marvell CXL device
DMA
controller
CXL
memory
GPU HBM
(VRAM)
descriptors
program ②
② PCIe P2P
① Submission
post descriptors (io_uring), spray to 16 queues, ring doorbell
② Execution
PCIe read/write direct to GPU HBM — no host DRAM / CPU / IOMMU
③ Completion
SQ↔CQ pairs; polled counter favors low latency
④ Pipelining
back-to-back; a core per queue keeps the link busy